## Slide 1
HPC SYSTEMS
RESEARCH REPRODUCTION
Locality-Aware
Task Scheduling
on Heterogeneous Architectures
AMD Opteron 8-Node NUMA
TILEPro64 8×8 Mesh
NOVA / ALLoC
DUAL ARCHITECTURE
NUMA
8-node
MESH
8×8
Local ~40 cyc · Remote 240–340 cyc
Local 10 cyc · Remote 38+2·h cyc
Reproducing Muddukrishna et al. (Scientific Programming 2015) — uncovering the SparseLU paradox and delivering NOVA co-scheduling.
Locality-Aware Task Scheduling on Heterogeneous HPC Architectures · 01 / 05

## Slide 2
PART 01
Two Memory Models,
Two Latency Cliffs
Discrete socket memory hierarchies vs. distributed shared L2 cache on an 8×8 mesh
AMD Opteron 8-Node NUMA
HyperTransport Interconnect · 3–6 cores/node · First-touch allocation
Topology: 8 sockets · 24–48 cores total
Local DRAM: ~40 CPU cycles (integrated IMC)
Remote Bus: 240–340 CPU cycles (6×–8× stall)
Diameter: 3 hops max · Failure: bus saturation
TILEPro64 8×8 Mesh
Manhattan hop distance · 64 tiles · 2D dynamic mesh
Topology: 8×8 grid · 1 VLIW core per tile
Local L2: 10 cycles · Remote: 38 + 2·h
Diameter: 14 hops = 66 cycles (opposite corner)
Failure: center bisection contention / home trap
cost(X) = Σ (D[i] / line_size) × latency(X, i) · locality dealing cuts stalls up to 80% — but starves idle cores when backlog is ignored!
Locality-Aware Task Scheduling · Hardware Topology & Latency Models · 02 / 05

## Slide 3
PART 02
Why Naive Locality Fails:
The 10 Hotspots
Deep audit of Muddukrishna et al. (2015) — root causes of runtime regression
Stealing & Placement
H1 – H4
• H1 Static Steal Reach: hard-coded vicinity starves threads on Map or drags remote stalls.
• H2 Queue-Level Stealing: pops victim tail blindly — ignores local-data tasks in same queue.
• H3 Load-Blind Placement: dealer routes to argmin(comm) without reading queue length.
• H4 Binary Threshold Cliffs: hard gates trigger O(N²) path with no calibration.
Data Model & Feedback
H5 – H7
• H5 Fragile Footprints: D relies on OpenMP depend clauses; incomplete clauses ruin placement.
• H6 No Feedback Loop: data frozen at omp_malloc; runtime never migrates hot mis-placed pages.
• H7 Coarse/Fine Menu Blind: rigid 2-item menu fails on irregular SparseLU blocks.
Mesh Bottlenecks
H8 – H10
• H8 Static Home-Cache Trapping: data locked to initial tile — brutal locality vs load trade-off.
• H9 Center Bisection Contention: XY routing concentrates traffic at tiles 3,3 → 4,4.
• H10 2D Coarse/Fine Mismatch: 1D line striping destroys 2D spatial locality for block solvers.
AUDIT DISCOVERY · Optimizing memory locality while ignoring queue backlog and interconnect contention is mathematically self-defeating on irregular task graphs.
Auditing Muddukrishna et al. (2015) · 10 Hotspots Taxonomy H1–H10 · 03 / 05

## Slide 4
PART 03
The SparseLU Paradox:
When Locality Slows Down
100 NUMA runs (8-node Opteron) + 56 TILEPro64 mesh configurations
1. AMD Opteron NUMA Reproduction (100 Runs)
• Map: −45.1% Comm · −19.0% Cycles • SparseLU: +15.1% SLOWER (Paradox!)
2. TILEPro64 8×8 Mesh Simulation (64 Cores)
• Map: −80.3% Comm Drop · 39.3% Speedup · 0 Steals vs 63 in WS baseline
THE EMPIRICAL LAW: Locality dealing cuts comm cost by up to 80.3%, but causes a +15.1% slowdown on irregular DAGs without load balancing.
Empirical Reproduction: AMD Opteron NUMA & TILEPro64 Manycore Mesh · 04 / 05

## Slide 5
PART 04
The NOVA Solution:
Adaptive Co-Scheduling
Four architectural pillars + defense takeaways — zero-contention control plane
N-A
Load-Aware Work Dealing
Fixes H3, H4
Composite score: α·comm_norm(D,q) + (1−α)·occ_norm(q) — balances proximity with backlog.
score(q) = α·comm_norm + (1−α)·occ_norm
N-B
Task-Level Shadow Index
Fixes H2
Lock-free ring buffer (k=8). Thief peeks top tasks — steals matching local RAM instead of blind tail-pop.
argmax_{t∈Top-K} Affinity(thief, Footprint(t))
N-C
Adaptive Vicinity Radius
Fixes H1
Per-worker EWMA adjusts reach: expands during starvation, contracts when balanced.
radius_{t+1} = clamp(radius_t + sign(rate_EWMA−target), 1, D_max)
N-D
Dynamic Migration & Zero Locks
Fixes H6, H8
Re-home lines when Acc_Benefit > C_mig (~120 cyc). Double-buffered CAS swap every 64 ops.
Trigger IF (Acc_Benefit > 120 cycles)
NOVA PRINCIPLE · Maximize memory locality when queues are balanced; dynamically transition to load-balancing when backlog threatens idle stalls.
NOVA / ALLoC Scheduler Architecture · High-Performance Computing · 05 / 05